Nitrous Oxide Transport and Transformation

Pierre-Andre Jacinthe

Department of Geology

Indiana University Purdue University Indianapolis (IUPUI)

Phone: 317-274-7969; Fax: 317-274-7966

Email: pjacinth@iupui.edu

Introduction and background:

Nitrous oxide (N2O) is a greenhouse gas and is also implicated in stratospheric ozone depletion.  Concentration of N2O in the atmosphere is 0.31 ppm (v/v) and is increasing at a rate of 0.25 % year-1.  Nitrous oxide is produced naturally via denitrification, a process whereby microbes in soils and sediments use nitrate (NO3-) as an alternative electron acceptor in anaerobic (O2-limited) environments.  In the subsurface and in the vadose zone, denitrification is responsible for the removal of NO3 contained in percolating waters.   Thus, denitrification could prevent NO3 from  reaching and contaminating groundwater systems.

Denitrification is a multi-step process involving (I) reduction of NO3 to nitrous oxide (N2O) and (ii) conversion of N2O to elemental nitrogen (N2).  Production and emission of N2O is a potential drawback for subsurface denitrification enhancement, given the impact of N2O on air quality.  However, if the N gases evolved during subsurface denitrification are converted to N2 before escaping into the atmosphere, subsurface denitrification enhancement would be a safe method to deal with excess NO3 in the environment.

Purpose

Several soil physical and biochemical soil properties could affect the transport and reduction of N2O in soils.  These include:

- diffusion: movement of gas through soils is determined by concentration gradient.  Rapid transport is generally assumed to be less conducive to reduction of N2O to N2.

- soil moisture content: Water occupies the same pore space available for diffusion of gases.  Diffusion through water is several orders of magnitude lower than through the gas phase.  Therefore, as water content increases, diffusion is restricted and the residence time of N2O in soil increases.  These conditions are more favorable to N2O reduction

- organic matter content: microbes involved in denitrification are heterotrophs, and therefore their activity depends on supply of organic carbon.

- N2O-reductase activity: This enzyme catalyzes the reduction of N2O to N2, and its activity is inhibited by acetylene (C2H2).  N2O reductase activity is generally assessed by comparing N2O production in samples exposed to C2H2 and in samples not exposed to C2H2.

Objectives

The purpose of this exercise is to identify and gain an understanding of soil factors controlling conversion of N2O during transport through soils.  Specifically, students will: 	- assess the impact of soil moisture content and N2O diffusion through soils

- examine relationships between soil properties and composition of N gases emitted (ie percentage of N2 and N2O)

Time required

This exercise can be completed during a 2-hour lab session.  However, this would require some preliminary work by the instructor to determine background soil properties.  Alternatively , the sequence of lab sessions could be such that students have gathered these background soil data during previous lab sessions.  This approach is preferred if time permits.

Material and Experimental setup

Instructor will collect undisturbed soil cores (L: 30 cm; diam: 15 cm) using PVC pipes.  Cores are to be collected at sites with contrasting land-uses (forest, grassland, cropland) and hydrology (well drained to poorly drained).  At each site, collect a set of 2 surface (< 40 cm depth) and a set of 2 deep (> 40 cm) cores.  Also collect smaller (L: 5 cm; diam: 5 cm) cores and disturbed soil samples for assessment of background soil properties.

- Drill the PVC pipes at 5, 10 and 20 cm depth and install a sampling port at each depth.

- Cap the bottom end of each core with a PVC cap fitted with a gas sampling/injection port.

- Near the top rim of the PVC pipe, place a collar with a groove to accommodate a lid.  The lid (headspace volume: 500 mL) is fitted with a sampling port and will be placed on top of the core during N2O flux measurement (Fig. 1).

To preserve moisture content, cover core openings with plastic wrap paper.  If cores are stored at cold temperature, take cores out of cold room and leave them in the lab the night before the lab session.

| Fig. 1. |  |
| --- | --- |

- Organize students into groups (2-3 students per group is optimal).

- Instructor will assign a set of 2 soil cores to each group.  Instructor will ascertain that the set of cores is from the same site x depth combination.

- Each group receives:

- a tedlar gas bag containing nitrous oxide (1000 ppm N2O);

- 3 syringes fitted with stopcock and hypodermic needle.  To avoid cross contamination, students are advised to use a different syringe-needle assembly for N2O injection and N2O sampling.

- 10 pre-evacuated gas vials (nominal volume 5 mL).

- Students are to label vials using a common labeling system so as to facilitate data sharing at the end of the exercise.  A system that includes group #, treatment applied, and location/time of sampling is suggested.  See examples below

G1-WA-H2 where, G1: group1; WA: with acetylene; H2: headspace at time2

G3- NA-D5 where, G3: group3; NA: no acetylene; D5: 5 cm depth

Procedure

- Attach inject the bottom of one of the cores to a C2H2 tank (10-20 % v/v).  Instructor will set pressure at ~15 psi and flow rate at ~ 40 mL min-1.  Let gas flow for 15 minutes.  Assuming porosity = 0.12 cm3 air cm-3 soil, that will correspond to approx. 1 pore volume.

- After 15 min, inject 100 ml of N2O in each core through the port located at 20 cm depth.

- After 1 hour, add some water into the groove (Fig. 1) and place the lid on top of each core to create a headspace.  Take 10 mL of air from each core headspace and store each sample in appropriately-labeled  vials.  Those are the time0 samples.

- After 30 more minutes, take another 10 mL sample from each core headspace and store them as described above.  These are the time1 samples.  At this time, also collect air samples (5 mL) from sampling ports located at 5 and 10 and 20 cm depths in each core.

- Wait for another 30 minutes, take the time2 samples for each core headspace.  Remove the lids.

- Submit air samples to the lab coordinator for gas chromatographic analysis.  Results are forwarded to the entire class.  Results are reported in ppm (v) which is equivalent to μL N2O L-1 air.

Computation

a) Diffusion coefficient

- N2O diffusion through cores (Ds) using the model of Rolston et al. (1976)

Ds = -k (VL/A)

ln [(Cs-Ca)/Cs] = -kt

where

Ds : diffusion coefficient (cm2 s-1),

V: chamber  volume(cm3),

A: cross-sectional area of the core (cm2),

L : thickness of the soil layer considered (cm) ,

Cs : concentration of N2O (μL L-1) at depth L cm

Ca : concentration of N2O (μL L-1) in chamber headspace at time t (second).

k: (second-1) is the slope of the plot (obtained by regression),

b) N2O flux

- Plot N2O concentration (μL N2O L-1 air) in core headspace against time (min), and record the regression coefficient (k, μL N2O L-1 air min-1).  The rate (F) of N2O efflux (μL N2O cm-2 min-1) is computed as F = k .(V/A), where V: volume of the core headspace (Liter) and A: cross sectional area of the core (cm2)

- Capacity of soil microbes to decompose N2O is computed as the difference between F(with C2H2) and F(without C2H2).

Reports

- Each group (of students) writes a report to describe the lab exercise and discuss the results.  Results are presented as a summary Table as well as graphs to show relationships between fN2O and (i) soil texture (ii) soil moisture content, (iii) total and mineralizable C and (iv) diffusion coefficient.

Illustrations

To illustrate this exercise, data from a similar experiment are provided in the attached Excel file.  Cores were taken from 3 soils (4 cores from each): Soil B (somewhat poorly drained), soil C (poorly drained) and soil H (well drained).   Dimensions of soil cores and chamber headspace are different, but computational approach is directly applicable to this exercise.

Reference

Rolston, D.E., M. Fried and D.A. Golhamer. 1976.  Denitrification measured directly from nitrogen and nitrous oxide gas fluxes.  Soil Science Society America Journal 40:259-266.