Hydrologic Cycle and Water Balance Equation

Directions:  Answer the following questions to the best of your abilities.  Where appropriate, show all of you work and use the appropriate significant figures.  The work for problem 2 and 3 will need to be completed using a spreadsheet (i.e. Excel) that will be submitted via e-mail.

- Create a conceptual model, including all possible inputs and outputs, for a 100 mi2 basin.  The basin annually receives 40 inches of rainfall.

- Using the conceptual model as a framework, develop an Excel model that calculates the runoff for a basin.  Note that individual components can be sub-divided, i.e. water that infiltrates can be used to recharge the ground water, can evaporate, or can be used by plants (transpiration).

  - Set up a spreadsheet program and calculate the total flux for each component in the water balance equation (provide components in inches/year, m3/day, and gallons/day – build your conversion factors into the spreadsheet).

  - You can use the following in your calculations:

    - 10% of precipitation goes to overland flow

    - 85% of precipitation infiltrates

    - Of the water that moves into the unsaturated zone, 40% goes to recharging the ground water and 40% is accounted for by evapotranspiration

    - Of the water that moves into the saturated zone, 95% goes to baseflow of streams within the basin

  - Check to see if your water balance equation is balanced.

  - Assume the average person consumes 200 gallons of water per day (this includes all uses such as personal, cooking, and development of goods and services used by a person).  As a result of governmental agreements, a minimum of 15 million gallons of water must leave the basin a stream flow each day.  Given the total runoff, how many people can this basin support?

- Assume that the mean annual temperature increases, resulting in a proportional increase in evapotranspiration.  Now assume that 70%, rather than 40%, of the unsaturated soil moisture results in ET and that 25%, rather than 40%, of the soil moisture goes to recharging the groundwater.  Furthermore, assume that 90% of the water in the saturated goes to baseflow of streams, instead of the 95%.

  - Create a second workbook that you can modify for the above problem. (You can copy the previous workbook and make modifications to the copy)

  - Modify the spreadsheet to account for these new flux rates.

  - Check to see if your water balance equation is balanced.

  - Compare and contrast the resulting ET and runoff rates derived for problems 4 & 5.

  - By what percent did streamflow change as compared to the first scenario?

  - Again, assume the average person consumes 200 gallons of water per day (this includes all uses such as personal, cooking, and development of goods and services used by a person).  As a result of governmental agreements, a minimum of 15 million gallons of water must leave the basin a stream flow each day.  Given the total runoff, how many people can this basin support?