Results from Darcy Column Demo

| Column No. | Material Type | Column Area (cm2) | Height of Material (cm) | Head Difference (cm) | Drained Volume (cm3) | Duration of Measurement (s) | Flow Rate (cm3/s) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 |  |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |  |

Darcy Column Lab

The purpose of this experiment is to demonstrate the relationship between flow rate, material type, head gradient, and flow area that is quantified with Darcy’s Law.

Equipment:

1 Darcy column (plastic bottle with lid and drain, filled with porous medium and water)

1 100 mL graduated cylinder

Cup filled with water

Funnel

Ruler

Stopwatch

Procedure:

- Note the material type – either sand, silt, or gravel.

- Determine the approximate flow area of the Darcy column.

- Measure the height of material in the column.

- Measure the head difference from the top of the porous material to the bottom of the porous material.

- Remove the cap from the bottle and insert the funnel into the top of the bottle.

- Measure the flow rate of water through the column as follows:

  - Simultaneously, hold the column over the graduated cylinder and remove the rubber stopper from the drain of the Darcy column; pour water from the cup into the bottle through the funnel, trying to maintain a constant head in the bottle; start the stopwatch.

  - Measured the amount of time required for a fixed amount of water to drain from the column into the graduated cylinder.

- Repeat Step 6 twice, and determine the average flow rate.

- Repeat Steps 1-7 for other bottles.