Cycles of the Sun and Moon

Step-By-Step Instructions

Part Two: Phases of the Moon

Download Moon Phase Data

- Go to the website for the Naval Observatory (http://aa.usno.navy.mil/data/index.html)

- Follow the link to the Dates of Primary Phases of the Moon

- Select the year from the links or enter it in the box.

- Convert the day/hour/minute to fractional day (i.e. 10/12/00 [d/h/m] would equal day 10.50).

- Assign the phase of Full Moon the value of +1; set New Moon equal to -1, and First and Last Quarters both equal to 0.

- Now, create a table in Excel that correlates the fractional day with the phase and graph it.

Example:

Curve Fitting

- Begin trying to fit a sine or cosine function to the graph of the moon phase.

REMEMBER:

If you start with the equation y=sin(x), you can adjust how it graphs by adding some constants to the equation.

If you add a constant to x [y=sin(x+a)], you can shift the graph as a whole left or right along the x axis depending on whether a is positive (left) or negative (right).

If you add constant to the whole right side [y=sin(x)+b] you can shift the graph as a whole up or down the y axis depending on whether b is positive (up) or negative (down).

If you add a multiplier to x [y=sin(cx)] you can adjust how closely placed the peaks and troughs of the graph are horizontally.  If c is between 0 and 1 (0<c<1), the distance from peak to peak will be larger than before.  If c is more than 1 (c>1), then the peaks will be closer together than before.

All three of these effects can work at the same time.  So if you add a negative constant a, a positive constant b and multiplier c>1 into the equation, the resulting graph will be shifted right and up from a normal sine function and the peaks will be closer together than normal.

- Once you have a sine function that matches well with the downloaded data points, create a plot of the function in Excel, including the final equation on the plot, and print out the graph to hand in.

Example: