# Example Projects

# Camp Lucas:

# Did the military leave objects buried on campus?

# unexploded ordinances, underground storage tanks, buried drums etc.

# (this project is described in more detail below as an example)

# Maple Ridge Cemetery

# Where are 100+ year old grave locations

# Records burned

City of Sault Ste Marie, MI wants to construct a fence around cemetery.  They do not want to errect the fence on top of grave sites.

# Determine depth to the water table and/or bedrock and or another horizon of interest.  May determine interface dip angle and direction and possible groundwater flow direction.

# Mineral exploration – potentially at a previous mining location or an area with economic potential

# Geologic bedrock mapping

# Where bedrock exposure is poor or non-existent

# Mid-continent rift geometry

# What is the thickness and geometry of Mid-continent igneous and sedimentary rocks?

Locating buried drums, tanks, contamination etc. at a industrial or commercial site.

This could be a local state, federal or privet site.

A brown field location may be appropriate.

Must chose a location that is safe for students to work

Below is an example of the project proposal, background and survey parameters I give my students for the Camp Lucas project.  I give nearly identical handouts with project specific content for the other projects described above.

# Example: Camp Lucas Project Proposal	Paul Kelso

# Lake Superior State University

Location of study area is southwest of the Norris Center, Lake Superior State University (LSSU)

Note location on Lake Superior State University campus map

124.1 acres were acquired in 1950 by U.S. military from the City of Sault Ste. Marie, MI

U.S. military returned the land to the city in the1960’s, part of which was transferred to LSSU

Concerns - did the military leave behind buried objects such as:

unexploded ordinances (UXO), buried drums, underground storage tanks (UST), bunkers, underground utilities, other buried materials

Camp Lucas/Fort Brady(WWI – WWII era fort) is the site of previous and ongoing environmental studies

Known UST’s were removed in the mid 1990’s

Ongoing study by U.S. Army Corps of Engineers, Michigan Department of Environmental Quality and environmental consulting company

Some of this material is available for your review on the geology network drive

Survey Design:

Determine which instrument(s) to use for survey

Why did you choose these instruments?

Why would this instrument likely record an anomaly (for each instrument)?

What are the likely anomalies characteristics you would expect with each instrument?

Design a survey lines/grid to achieve the above goals

Why did you choose this survey design?

Determine station spacing

Why did you choose this configuration?

It may be different for different instruments

Models of potential anomalies

Develop forward models for one or more examples of expected anomalies

Use realistic values for the materials’ geophysical properties

Models must be developed for each instrument suggested

Models must be presented for all proposed instruments

Costs

Personnel, equipment, overheat, profit, etc.   (see Planning a Geophysical Survey below)

You will have four geophysics field crews (3-4 people each) to collect data for this project during

three afternoons or one full day

Project Proposal Assignment (Group assignments):

Description of your project proposal (minimum 2 pages per group plus figures)

Model anomalies with figure captions must be included in addition to two pages of text

15 min. presentation of your proposal to class

All students must give part of presentation

Include detailed answers to all of the above questions

Above issues must be included/considered

Information provided prior to field survey

Overview of physical principles of potential techniques

(gravity, magnetics, electromagnetics, ground penetrating radar, resistivity, induced polarization, self potential, seismic refraction)

Basic equations and/or software for forward modeling of body geophysical responses for likely methods

Introduction to operation of equipment available for project

Including how long measurements take

Survey consideration

Brainstorm, think-pair-share or I may provide this  (see below)

# Planning a Geophysical Survey 			Paul Kelso

# Lake Superior State University

## Things to consider/include in a project proposal

Survey objectives

Geophysical target

Geophysical responses to target

Anomaly amplitude

Anomaly half width

Costs  (ultimately Financial, e.g.,  Thomas Boyd’s web site http://galitzin.mines.edu/INTROGP/index.jsp)

Personnel

Field time – including travel, set up, survey execution

Processing time

Reports, presentations- including preparation time

Operating costs - logistics

Equipment

Geophysical instruments, computers, vehicles, etc.

Purchase, rent, subcontract?

Software purchase/lease

Training – equipment, software, etc.

Contingencies – for unexpected complications – not if but when

Overhead – administration, insurance, building, facilities, consumables, etc.

This is usually calculated as a % of above expenses (50-100%)

Profit – how much are you going to make?

Logistics

Transportation to survey location

Access to survey area (terrain, weather, permission, etc.)

Political, social and religious considerations

Supplies, food, shelter, etc.

Survey Design

Geophysical methods

What instruments are you going to use and why?

What are the anomaly characteristics you expect with each geophysical technique?

Profiling vs. mapping

Station spacing

Spatial aliasing

Temporal aliasing  (base stations and seismics)

Line configurations

Line orientation - considerations

Perpendicular to strike, VLF source direction

Line spacing

Smaller than the width of the body of interest

Line length

Must be longer than anomaly so one can recognize the background signal

Tie lanes

To check the reproducibility of data

Noise

Common sources:  coherent vs. incoherent noise