Exercise 1 - Instructor Key

1) Stream cross-section

2) Discharge = 450 ft3/sec

|  | Stream Discharge Exercise |  |  |  |
| --- | --- | --- | --- | --- |
| n | b | width | depth | area | vel | Q |
| 0 | 0.0 |  |  |  |  |  |
| 1 | 2.0 | 2.50 | 0.00 | 0.0 | 0 | 0.00 |
| 2 | 7.0 | 5.00 | 0.91 | 4.6 | 0.9 | 4.10 |
| 3 | 12.0 | 5.00 | 0.93 | 4.7 | 1 | 4.65 |
| 4 | 17.0 | 5.00 | 1.81 | 9.1 | 1.09 | 9.86 |
| 5 | 22.0 | 3.75 | 2.67 | 10.0 | 1.21 | 12.12 |
| 6 | 24.5 | 2.50 | 2.69 | 6.7 | 1.19 | 8.00 |
| 7 | 27.0 | 2.50 | 2.56 | 6.4 | 1.24 | 7.94 |
| 8 | 29.5 | 2.50 | 2.54 | 6.4 | 1.46 | 9.27 |
| 9 | 32.0 | 3.75 | 2.61 | 9.8 | 1.73 | 16.93 |
| 10 | 37.0 | 5.00 | 2.47 | 12.4 | 2.67 | 32.97 |
| 11 | 42.0 | 5.00 | 2.47 | 12.4 | 2.51 | 31.00 |
| 12 | 47.0 | 5.00 | 2.46 | 12.3 | 2.55 | 31.37 |
| 13 | 52.0 | 5.00 | 2.47 | 12.4 | 2.43 | 30.01 |
| 14 | 57.0 | 4.00 | 2.59 | 10.4 | 2.41 | 24.97 |
| 15 | 60.0 | 3.00 | 2.63 | 7.9 | 2.45 | 19.33 |
| 16 | 63.0 | 3.00 | 2.74 | 8.2 | 2.52 | 20.71 |
| 17 | 66.0 | 3.50 | 2.68 | 9.4 | 2.45 | 22.98 |
| 18 | 70.0 | 4.50 | 2.66 | 12.0 | 2.32 | 27.77 |
| 19 | 75.0 | 5.00 | 2.47 | 12.4 | 2.49 | 30.75 |
| 20 | 80.0 | 5.00 | 2.48 | 12.4 | 2.37 | 29.39 |
| 21 | 85.0 | 5.00 | 2.31 | 11.6 | 2.22 | 25.64 |
| 22 | 90.0 | 5.00 | 1.90 | 9.5 | 2.05 | 19.48 |
| 23 | 95.0 | 5.00 | 1.81 | 9.1 | 1.89 | 17.10 |
| 24 | 100.0 | 5.00 | 1.80 | 9.0 | 1.52 | 13.68 |
| 25 | 105.0 | 2.50 | 0.00 | 0 | 0 | 0.00 |
|  |  |  |  |  | Qtotal= | 450.02 |

3)	Tributary A: Q = 1,206 - 1,100 ft3/sec = 106 ft3/sec

Tributary B: Q = 1,584 - 1,443 ft3/sec = 141 ft3/sec

Groundwater baseflow between tributaries:  Q = 1,443 - 1,206 ft3/sec = 237 ft3/sec

4) Could directly measure the discharge of the tributary itself.  The advantage of the first method is that it allows you to determine BOTH the tributary discharge AND the groundwater baseflow between any two tributaries.

5) To determine total groundwater baseflow for a small watershed you would need to measure stream discharge at the mouth of the basin in question (assumes no underflow).  Also, there must NOT have been any precipitation events during this time which could have led to runoff entering the system.

Exercise 2 - Instructor Key

1) Same as instructor key in Exercise #1

2a) Field Data

Stream Discharge Field Data

Location: Canoochee River at 301 Bridge near Claxton	Date: 9/19/2003

| n (station) | b (distance – ft) | d (depth - ft) | V1 (vel – ft/s) | V2 | V3 | Vave |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | 0 |  |
| 1 | 2.0 | 0 | 0 | 0 | 0 |  |
| 2 | 4.0 | 0.90 | 0.46 | 0.42 | 0.40 | 0.43 |
| 3 | 6.0 | 1.60 | 0.68 | 0.59 | 0.61 | 0.63 |
| 4 | 10.0 | 2.30 | 0.90 | 0.98 | 0.93 | 0.94 |
| 5 | 16.0 | 2.50 | 1.30 | 1.22 | 1.10 | 1.21 |
| 6 | 22.0 | 2.35 | 0.83 | 0.86 | 1.07 | 0.92 |
| 7 | 26.0 | 1.80 | 1.16 | 1.10 | 1.10 | 1.12 |
| 8 | 32.0 | 1.75 | 1.79 | 1.70 | 1.65 | 1.71 |
| 9 | 38.0 | 1.40 | 1.36 | 1.40 | 1.42 | 1.39 |
| 10 | 44.0 | 1.05 | 1.18 | 1.24 | 1.20 | 1.21 |
| 11 | 48.0 | 0.95 | 0.91 | 0.95 | 0.82 | 0.89 |
| 12 | 51.0 | 0.80 | 0.49 | 0.38 | 0.45 | 0.44 |
| 13 | 54.0 | 0.50 | 0 | 0 | 0 | 0 |
| 14 | 57.0 | 0.75 | 0 | 0 | 0 | 0 |
| 15 | 61.3 | 0 | 0 |  |  |  |

b) Spreadsheet Results

|  |  | Stream Discharge Exercise (Sept 19, 2003) |
| --- | --- | --- |
| 301 Bridge 1-1 |  |  |  |  |  |
| n | b | width (ft) | Depth (ft) | Area (ft2) | ave. vel (ft/s) | Discharge (ft3/s) |
| 0 | 0.0 |  |  |  |  |  |
| 1 | 2.0 | 1.00 | 0.00 | 0.0 | 0.00 | 0.00 |
| 2 | 4.0 | 2.00 | 0.90 | 1.8 | 0.43 | 0.77 |
| 3 | 6.0 | 3.00 | 1.60 | 4.8 | 0.63 | 3.01 |
| 4 | 10.0 | 5.00 | 2.30 | 11.5 | 0.94 | 10.78 |
| 5 | 16.0 | 6.00 | 2.50 | 15.0 | 1.21 | 18.15 |
| 6 | 22.0 | 5.00 | 2.35 | 11.8 | 0.92 | 10.81 |
| 7 | 26.0 | 5.00 | 1.80 | 9.0 | 1.12 | 10.08 |
| 8 | 32.0 | 6.00 | 1.75 | 10.5 | 1.71 | 17.96 |
| 9 | 38.0 | 6.00 | 1.40 | 8.4 | 1.39 | 11.68 |
| 10 | 44.0 | 5.00 | 1.05 | 5.3 | 1.21 | 6.35 |
| 11 | 48.0 | 3.50 | 0.95 | 3.3 | 0.89 | 2.97 |
| 12 | 51.0 | 3.00 | 0.80 | 2.4 | 0.44 | 1.06 |
| 13 | 54.0 | 3.00 | 0.50 | 1.5 | 0.00 | 0.00 |
| 14 | 57.0 | 3.65 | 0.75 | 2.7 | 0.00 | 0.00 |
| 15 | 61.3 | 2.15 | 0.00 | 0.0 | 0.00 |  |
|  |  |  |  |  | Qtotal= | 93.60 |

3) Replicate set of field data for statistical analysis

average discharge = 2.42 ft3/sec

| 301 Bridge (A) | 1/25/2002 |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| n | b | width | depth | area | vel | Q (ft3/s) |
| 0 | 0.0 |  |  |  |  |  |
| 1 | 2.8 | 1.00 | 0.60 | 0.6 | 0.00 | 0.00 |
| 2 | 4.8 | 2.00 | 0.95 | 1.9 | 0.00 | 0.00 |
| 3 | 6.8 | 2.00 | 0.70 | 1.4 | 0.25 | 0.35 |
| 4 | 8.8 | 2.00 | 0.79 | 1.6 | 0.39 | 0.62 |
| 5 | 10.8 | 2.00 | 0.76 | 1.5 | 0.49 | 0.74 |
| 6 | 12.8 | 2.00 | 0.72 | 1.4 | 0.43 | 0.62 |
| 7 | 14.8 | 2.10 | 0.50 | 1.1 | 0.16 | 0.17 |
| 8 | 17.0 | 1.10 | 0.00 | 0 | 0.00 | 0.00 |
|  |  |  |  |  | Qtotal | 2.50 |

| 301 Bridge (B) | 1/25/2002 |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| n | b | width | depth | area | vel | Q (ft3/s) |
| 0 | 1.8 |  | 0 |  |  |  |
| 1 | 2.8 | 1.00 | 0.60 | 0.6 | 0.00 | 0.00 |
| 2 | 4.8 | 2.00 | 0.92 | 1.8 | 0.00 | 0.00 |
| 3 | 6.8 | 2.00 | 0.70 | 1.4 | 0.20 | 0.28 |
| 4 | 8.8 | 2.00 | 0.80 | 1.6 | 0.41 | 0.66 |
| 5 | 10.8 | 2.00 | 0.75 | 1.5 | 0.48 | 0.72 |
| 6 | 12.8 | 2.00 | 0.70 | 1.4 | 0.43 | 0.60 |
| 7 | 14.8 | 2.10 | 0.55 | 1.2 | 0.17 | 0.20 |
| 8 | 17.0 | 1.10 | 0.00 | 0 | 0.00 | 0.00 |
|  |  |  |  |  | Qtotal | 2.45 |

| 301 Bridge (C) | 1/25/2002 |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| n | b | width | depth | area | vel | Q (ft3/s) |
| 0 | 0.8 |  |  |  |  |  |
| 1 | 2.8 | 1.00 | 0.60 | 0.6 | 0 | 0.00 |
| 2 | 4.8 | 2.00 | 0.92 | 1.8 | 0 | 0.00 |
| 3 | 6.8 | 2.00 | 0.70 | 1.4 | 0.21 | 0.29 |
| 4 | 8.8 | 2.00 | 0.78 | 1.6 | 0.36 | 0.56 |
| 5 | 10.8 | 2.00 | 0.72 | 1.4 | 0.47 | 0.68 |
| 6 | 12.8 | 2.00 | 0.68 | 1.4 | 0.43 | 0.58 |
| 7 | 14.8 | 2.10 | 0.52 | 1.1 | 0.17 | 0.19 |
| 8 | 17.0 | 1.10 | 0.00 | 0 | 0 | 0.00 |
|  |  |  |  |  | Qtotal | 2.30 |

4)	Standard deviation = 0.104 ft3/sec

Average discharge = 2.42 ft3/sec

Percent error = 4.3%