AN ANALOG MODEL OF AN EARTH DAM

Horacio Ferriz, Don Siegel, Solomon Isiorho, Tom Lachmar,

Joe Yelderman, Devin Castendyk

Goal: To document the geometry of the water table across an earth dam.

Materials:

A sheet of ¼ inch plywood, a sheet of plexiglass, silicon caulking, ½ inch strips of plexiglass, aquarium gravel, sand, silty sand, clay, mesh.

Setup:

- Fit the plywood and plexiglass with the studs. Fit the sides with the strips of plexiglass, and caulk them in place. Do a good job and you can use the same box over and over.

- Fill in the materials as shown in the diagram. Moisten the sediments a little, and tamp them gently in lifts of 1 or 2 inches. Use the mesh as needed to avoid slumping.

- Fill in the reservoir and you are ready to play!

What to do?

- Convince yourself that water flows down hydraulic gradient, and not down dip!

- Convince yourself that hydraulic gradient becomes steeper as hydraulic conductivity decreases. Why is this?

- Try drawing some flow lines on the plexiglass (use a water soluble marker!).

- Why did the engineer build a key under the clay core of the dam?

- Why is there a forebay?

- This dam is not really impermeable, is it? What is its purpose then?